## Slide 1: Conducting Research in Space – A Journey Towards the International Space Station
Dr. Brock J. LaMeres
Associate Professor
Electrical & Computer Engineering

## Slide 2: What I’d Like to Share Tonight
Motivation for Conducting Research in Space
Common Mechanisms to Get to (or almost) Space
My Research in Space Computer Systems
Existing/Future MSU Missions

## Slide 3
1) Motivation for
Research in Space

## Slide 4: First, What is Space?
Definition: The Region beyond Earth’s Atmosphere Webster’s
Most agree space starts at 100 km (328,000 ft, 62 miles) above sea level

## Slide 5: Some Perspective

## Slide 6: More Perspective
Common Orbits
To the Moon, 384,000 km

## Slide 7: More Perspective
Common Orbits
Famous Stuff in LEO
To the Moon, 384,000 km

## Slide 8: More Perspective
Common Orbits
Famous Stuff in LEO
Famous Stuff in ~GEO
ComSats
GPS
To the Moon, 384,000 km

## Slide 9: The Space Environment: Atmosphere
As we go higher, the atmosphere diminishes…
You Are Here
At 100,000 feet you are out of 99% of the atmosphere
This altitude is reached thousands of time per day by weather balloons (~200/day in the US)

## Slide 10: The Space Environment: Atmosphere
Our Atmosphere is incredibly THIN…
Radius of the Earth (Re)
6,371 km
Atmosphere
+100km
(1.5% of Earth’s Radius)

## Slide 11: The Space Environment: Gravity
As we go higher, gravity diminishes…
gh = new gravitational acceleration
h = height above sea level
Re = radius of the Earth
g0 = Earth gravitational acceleration
Re
Re + h
gh = g0

## Slide 12: The Space Environment: Gravity
But you have to be really far away for micro-gravity, right?
1 g0
1/4 g0
1/9 g0
Re
2Re
3Re
1/16 g0
4Re
6,371 km
12,742
km
19,113
km
1/25 g0
5Re
25,484
km
1/36 g0
6Re
1/49 g0
7Re
31,855
km
38,226
km
Altitude
0
km
To the Moon, ~107 Re
Low Earth Orbit

## Slide 13: The Space Environment: Gravity
But you have to be really far away for micro-gravity???
1 g0
1/4 g0
1/9 g0
Re
2Re
3Re
1/16 g0
4Re
6,371 km
12,742
km
19,113
km
1/25 g0
5Re
25,484
km
1/36 g0
6Re
1/49 g0
7Re
31,855
km
38,226
km
Altitude
0
km
Low Earth Orbit
But I’ve seen Astronauts Floating?
?
To the Moon,
~107 Re

## Slide 14: The Space Environment: Gravity
The key is the word “orbit”
We can use the concept of centripetal force to keep our space craft aloft at low altitudes if we get them going fast enough.
Once in orbit, everything experiences the same “free fall” force toward the Earth. Thus an orbit mimics zero-gravity just like sky divers experience.

## Slide 15: The Space Environment: Temperature
As we go higher, the temperature variation is HUGE…
Cools down because of thinning air.
Warms up due to ozone concentration absorbing UV light.
Cools down again because of lack of ozone.
Warms up again due to molecular oxygen absorbing sunlight but not enough air to dissipate heat.
You Are Here

## Slide 16: The Space Environment: Temperature
In LEO, the temperature goes from:
-157 C (-250 F)
At
Night
+121 C (+250 F)
During the
Day
The ISS experiences 15-16 sunrises & sunsets per day!

## Slide 17: The Space Environment: Radiation
As we go higher, the radiation increases…
Outside of the Earth’s magnetosphere, cosmic rays and low energy electron/protons are not blocked/deflected.
Between 0-100,000 ft, the atmosphere thins and doesn’t block alpha, beta, gamma

## Slide 18: The Space Environment: Radiation
The magnetosphere is large…
* Normal solar weather conditions
Re
2Re
3Re
4Re
6,371
12,742
19,113
5Re
25,484
6Re
7Re
31,855
38,226
Altitude
(km)
0
Re
2Re
3Re
4Re
6,371
12,742
19,113
0
LEO
LEO

## Slide 19: The Space Environment: Radiation
But there are regions where the magnetosphere’s protection dips at lower altitudes
Re
2Re
6,371
0
2,000
Altitude
(km)

## Slide 20: Motivation for Research in Space
It provides an environment that is difficult to reproduce on Earth
No Atmosphere
Micro Gravity
Extreme Hot / Cold
High Radiation
But what science needs that?

## Slide 21: Motivation for Research in Space

## Slide 22
2) OK I’m in, how do I get there?

## Slide 23: Space Vehicles: Balloons
1) Balloons – Not exactly space, but they can provide extreme environments
BOREALIS

## Slide 24: Space Vehicles: Sounding Rockets
2) Sounding Rockets – Technically space, but no orbit.

## Slide 25: Space Vehicles: Small Satellites
3) Small Satellites
  Orbital missions in LEO can last weeks to 2 years
  CubeSats are all the rage right now (1U, 3U, 6U where U=100mm3).
Hiscock Radiation Belt Explorer (HRBE)
Vehicles can be Taurus XL, Delta 2, etc…

## Slide 26: Space Vehicles: ISS
4) International Space Station
  Started in 1998. Completed in 2011. It is dedicated to science in all forms.

## Slide 27: Space Vehicles: An Example
One Example of a Provider (NanoRacks)
  Full service $15k-$30k for 1U CubeSat. Launches off ISS
NanoRack CubeSat Deployer

## Slide 28
3) So what is your involvement?

## Slide 29: What is Reconfigurable Computing?
A System That Alters Its Hardware as its Normal Operating Procedure
  This can be done in real-time or at compile time.
  This can be done on the full-chip, or just on certain portions.
  Changing the hardware allows it to be optimized for the application at hand.
The typical approach to hardware is to build everything that will ever be needed.
In Reconfigurable Computing, hardware is instead altered and re-used.

## Slide 30: What is Reconfigurable Computing
A System That Alters Its Hardware as its Normal Operating Procedure
  This can be done in real-time or at compile time.
  This can be done on the full-chip, or just on certain portions.
  Changing the hardware allows it to be optimized for the application at hand.
Today’s Computers are Based on a General-Purpose Processor
  The GP CPU is designed to do many things.
  This is the “Jack of All Trades, Master of None” approach.
General Purpose CPU Model
Reconfigurable Computing Model

## Slide 31: Who Cares?
Our Existing Computers Seem to be Working Well. Why Change?
  Our existing computers have benefited from 40 years of Moore’s Law.
  In the 1960’s, Gordon Moore predicted that the number of transistors on a chip would double every ~24 months.
Gordon Moore, co-founder of Intel, holding a vacuum tube.
1959 - 1965
1971* - 2011
Note: First microprocessor introduced in 1971,
the Intel 4004 with 2300 transistors.
Intel 4004 (2300 T)
Intel Xeon (2B T)

## Slide 32: How long can we do this?
When will Moore’s Law End?
  Most exponentials do come to an end.
Clock Speed
Power
Performance per Clock Cycle
But is transistor count what we care about?

## Slide 33: Computation vs. Transistor Count
We Really Care About Computation
You Are Here

## Slide 34: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.

## Slide 35: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.

## Slide 36: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.

## Slide 37: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.
  They need to operate in the presence of harsh radiation.
Can you repeat the question???

## Slide 38: Where Does Radiation Come From?
3) Trapped Radiation
1) Cosmic Rays
2) Solar Particle Events

## Slide 39: What are the Effects?
1. Total Ionizing Dose (TID)
      Cumulative long term damage due to ionization.
      Primarily due to low energy protons and electrons due to higher, more constant flux, particularly when trapped
      Problem #1 – Oxide Breakdown
        Threshold Shifts
        Leakage Current
        Timing Changes
2. Single Event Effects (SEE)
      Electron/hole pairs created by a single particle passing through semiconductor
      Primarily due to heavy ions and high energy protons
      Excess charge carriers cause current pulses
      Creates a variety of destructive and non-destructive damage “Critical Charge” = the amount of charge deposited to change the state of a gate

## Slide 40: But I’m Texting Right Now?
How can our computers function?
You Are Here
Thank you atmosphere. Thank you magnetosphere

## Slide 41: But there are computers in space?
Stuff is in space now, how does it function?
Rad-Hard Processors Can be Made that are SLOW and EXPENSIVE
  Rad-Hard computers tend to lag commercial versions in performance by 10+ years.
  They are also 100s-1000x more expensive.
Thank you federal government.
A-Side Computer
BAE Rad750 $200,000
B-Side Computer
BAE Rad750 $200,000

## Slide 42: I Know You’re Going to Ask….
Can’t you just add shielding?
  Shielding helps for protons and electrons <30MeV, but has diminishing returns after 0.25”.
  This shielding is typically inherent in the satellite/spacecraft design, meaning the most optimal amount of shielding is usually present in the shell of the spacecraft.
Shield Thickness vs. Dose Rate (LEO)

## Slide 43: How Does RC Help This?
Total Ionizing Dose
  TID actually diminishes as features get smaller.
  This is good because we want to use the smallest transistors to get the fastest performance.
  Using off-the-shelf parts also reduces cost.
Single Event Effects
  SEE gets worse! But it isn’t permanent.
  So we just need a new computer architecture to handle it.

## Slide 44: Enter MSU
FPGA-Based, Radiation Tolerant Computer
  The FPGA is divided up into Tiles
  A Tile is a quantum of resources that:
      Fully contains a system (e.g., processor, accelerator)
      Can be programmed via partial reconfiguration (PR)
Fault Tolerance
  TMR + Spares
  Spatial Avoidance of Background Repair
  Scrubbing
  An External Radiation Sensor
16 Tile System on an Xilinx Virtex-6

## Slide 45: Technical Readiness Level (TRL-1)
Step 1 – Understand the Problem and See if RC Helps
  The Montana Space Grant Consortium funds an investigation into conducting radiation tolerant computing research at MSU. The goal is to understand the problem, propose a solution, and build relationships with scientists at NASA.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
2009
2008
Timeline of Activity at MSU
Clint Gauer (MSEE from MSU 2009) demo’s computer to MSFC Chief of Technology Andrew Keys

## Slide 46: Technical Readiness Level (TRL-3)
Step 2 – Build a Prototype and Test in a Cyclotron
  NASA funds the development of a more functional prototype and cyclotron testing .
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
(2010-2012)
2009
2008
Timeline of Activity at MSU

## Slide 47: Technical Readiness Level (TRL-5)
Step 3 – Demonstrate as Flight Hardware on High Altitude Balloons
  NASA funds the development of the computer into flight hardware for demonstration on high altitude balloon systems, both in Montana and at NASA.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
(2010-2012)
(2011-2013)
2009
2008
Timeline of Activity at MSU
MSU Computer
Justin Hogan (Ph.D., EE from MSU, 2014) prepares payload.

## Slide 48: Technical Readiness Level (TRL-7)
Step 4 – Demonstrate as Flight Hardware on a Sounding Rocket
  Flew to an altitude of 124 km (408,000 ft)
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
(2010-2012)
(2011-2013)
(2012-2014)
2009
2008
Timeline of Activity at MSU

## Slide 49: Technical Readiness Level (TRL-8)
Step 5 – Demonstrate on the International Space Station
  NASA funds the demonstration of computer system in International Space Station.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
(2010-2012)
(2011-2013)
(2012-2014)
(2014-2015)
2009
2008
Timeline of Activity at MSU
ISS Mockup at Johnson Space Center for Crew Training
Mission Control Room for Apollo Program

## Slide 50: Technical Readiness Level (TRL-8)
Selfie with $60M Space Suit

## Slide 51: Technical Readiness Level (TRL-9)
Step 6 – Demonstrate as a Stand-Alone Satellite
  NASA funds the demonstration of the computer system in a Low Earth Orbit mission.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
Satellite
Demo
(2010-2012)
(2011-2013)
(2012-2014)
(2014-2015)
(2014-2016)
2009
2008
Timeline of Activity at MSU

## Slide 52: Technical Readiness Level (TRL-9)
Step 7 – Commercialize It
  License Agreement with 406 Aerospace, LLC, Bozeman, MT.

## Slide 53: MSU Students Did it Alll
Everything was Designed and Built By MSU Students!
Todd Buerkle, Justin Hogan, Ray Weber at Johnson Space Center for demo, 2012.
Todd Buerkle, Jennifer Hane at the Marshall Space Flight Center, 2011.
Justin Hogan at the NASA Columbia Scientific Balloon Facility, 2012.
Justin Hogan & Ray Weber featured in MSU News Story, 2012.
Clint Gauer demo’s computer at Marshall Space Flight Center, 2009.
Todd Buerkle & Jennifer Hane demo computer at Marshall Space Flight Center, 2012.
Clint Gauer at Marshall Space Flight Center for demo, 2009.
Kaysha Young prepares payload for balloon flight, 2012.
2013 balloon team recovers payload in front of moose, 2013.
2011 balloon team featured in MSU news story, 2011.

## Slide 54
4) Other Missions from MSU

## Slide 55: Microbiology – Microgravity Exp.

## Slide 56: Physics – Long Term Exposure Exp.

## Slide 57
  Thank You

## Slide 58: References
Content
  “Space Transportation Costs: Trends in Price Per Pound to Orbit 1990-2000. Fultron Inc Technical Report., September 6, 2002. Sammy Kayali, “Space Radiation Effects on Microelectronics”, JPL, [Available Online]: http://parts.jpl.nasa.gov/docs/Radcrs_Final.pdf.
  Holmes-Siedle & Adams, “Handbook of Radiation Effects”, 2nd Edition, Oxford Press 2002.
  Thanh, Balk, “Elimination and Generation of Si-Si02 Interface Traps by Low Temperature Hydrogen Annealing”, Journal of Electrochemical Society on Solid-State Science and Technology, July 1998.
  Sturesson TEC-QEC, “Space Radiation and its Effects on EEE Components”, EPFL Space Center, June 9, 2009. [Available Online]: http://space.epfl.ch/webdav/site/space/shared/industry_media/07%20SEE%20Effect%20F.Sturesson.pdf
  Lawrence T. Clark, Radiation Effects in SRAM: Design for Mitigation”, Arizona State University, [Available Online]: http://www.cmoset.com/uploads/9B.1-08.pdf
  K. Iniewski, “Radiation Effects in Semiconductors”, CRC Press, 2011.
Images
  If not noted, images provided by www.nasa.gov or MSU
  Displacement Image 1: Moises Pinada, http://moisespinedacaf.blogspot.com/2010_07_01_archive.html
  Displacement Image 2/3: Vacancy and divacancy (V-V) in a bubble raft. Source: University of Wisconsin-Madison
  SRAM Images: Kang and Leblebici, "CMOS Digital Integrated Circuits" 3rd Edition. McGraw Hill, 2003
  SEB Images: Sturesson TEC-QEC, “Space Radiation and its Effects on EEE Components”, EPFL Space Center, June 9, 2009.
  FPGA Images: www.xilinx.com, www.altera.com
  RHBD Images: Giovanni Anelli & Alessandro Marchioro, “The future of rad-tol electronics for HEP”, CERN, Experimental Physics Division, Microelectronics Group, [Available Online]:

## Slide 59: References
Images
  If not noted, images provided by www.nasa.gov or MSU - SL9 rocket - astronaut at observation window
  (earth n moon) Space at 50, National Geographic
  Aspen Global Change Institute | The Atmospherewww.agci.org
  (alt with Spaceship1) Will space tourism ever be a reality? - HowStuffWorksscience.howstuffworks.com
  (alt vs. whats there) Atmospheric Structure, www.albany.edu
  (comsat) GPS navigáció - navigációs rendszerek | Felsofokon.hu, www.felsofokon.hu
  (alt v pres) Diagram Of Atmospheric Pressure Vs Altitude Royalty, www.dreamstime.com
  (xsection of earth) Introduction to Geography: Physical Attributes of Earthâ€™s Landscapeaventalearning.com
  (Gravity vs. Re) http://www.physicsclassroom.com/class/circles/Lesson-3/The-Value-of-g
  (Centripetal Force) Aerospaceweb.org | Ask Us - Space Shuttle Speed in Orbitwww.aerospaceweb.org
  (Temp vs. Altitude) Los Angeles Pierce College Weather Stationdata.piercecollege.edu
  (SAA Figure) The Bermuda Triangle of Space: The High-Energy South Atlantic ...archive.defensenews.com